## Slide 1: CCD Astronomy
Jeff Thrush
www.sliderbase.com
Notes: CCD Astronomy
Jeff Thrush
CCD Astronomy
Jeff Thrush

## Slide 2: Optical Sensors used in Astronomy
Human Eye
  For most of history the practical sensor has been the human eye.
  Limited by Sensitivity
  Physiological considerations and human subjectivity, placed serious limits on what could be discovered.
Photographic Films
  The advent of photography in the last century was a monumental step forward in astronomy
  It has the ability to record “unseeable” objects with long exposure times
  Despite improvements, its efficiency remains very low.
    For every 100 photons that strike the film, at best only three or four react with the silver in the film’s emulsion
    Reciprocity failure
www.sliderbase.com
Notes: Optical Sensors used in Astronomy
Human Eye
For most of history the practical sensor has been the human eye.
Limited by Sensitivity
Physiological considerations and human subjectivity, placed serious limits on what could be discovered.
Photographic Films
The advent of photography in the last century was a monumental step forward in astronomy
It has the ability to record “unseeable” objects with long exposure times
Despite improvements, its efficiency remains very low.
For every 100 photons that strike the film, at best only three or four react with the silver in the film’s emulsion
Reciprocity failure
Optical Sensors used in Astronomy
Human Eye
For most of history the practical sensor has been the human eye.
Limited by Sensitivity
Physiological considerations and human subjectivity, placed serious limits on what could be discovered.
Photographic Films
The advent of photography in the last century was a monumental step forward in astronomy
It has the ability to record “unseeable” objects with long exposure times
Despite improvements, its efficiency remains very low.
For every 100 photons that strike the film, at best only three or four react with the silver in the film’s emulsion
Reciprocity failure

## Slide 3: My Telescope “1979”
www.sliderbase.com
Notes: My Telescope “1979”
My Telescope “1979”

## Slide 4: Optical Sensors used in Astronomy
Charged Coupled Device (CCD)
  With better than 20% efficiency, they quickly won over the astronomical community
  There sensitivity extends into the infrared spectrum
  Its response to light is a linear function of incident flux and exposure time.
    There is no reciprocity failure as encountered in long duration astrophotographs
www.sliderbase.com
Notes: Optical Sensors used in Astronomy
Charged Coupled Device (CCD)
With better than 20% efficiency, they quickly won over the astronomical community
There sensitivity extends into the infrared spectrum
Its response to light is a linear function of incident flux and exposure time.
There is no reciprocity failure as encountered in long duration astrophotographs
Optical Sensors used in Astronomy
Charged Coupled Device (CCD)
With better than 20% efficiency, they quickly won over the astronomical community
There sensitivity extends into the infrared spectrum
Its response to light is a linear function of incident flux and exposure time.
There is no reciprocity failure as encountered in long duration astrophotographs

## Slide 5: A CCD camera can provide a personal window to the universe or total frustration
www.sliderbase.com
Notes: A CCD camera can provide a personal window to the universe or total frustration
A CCD camera can provide a personal window to the universe or total frustration

## Slide 6: CCD Camera “Buzz” Words
CCD Arrays
Sampling
Pixels
Sensitivity
Pixel Binning
Blooming vs. Anti-Blooming
Readout Noise
Gain
Thermal Noise
Quantum Efficiency
www.sliderbase.com
Notes: CCD Camera “Buzz” Words
CCD Arrays
Sampling
Pixels
Sensitivity
Pixel Binning
Blooming vs. Anti-Blooming
Readout Noise
Gain
Thermal Noise
Quantum Efficiency
CCD Camera “Buzz” Words
CCD Arrays
Sampling
Pixels
Sensitivity
Pixel Binning
Blooming vs. Anti-Blooming
Readout Noise
Gain
Thermal Noise
Quantum Efficiency

## Slide 7: The first questions you should ask yourself
What kind of imaging are you interested in doing
  The selection of your camera depends strongly on whether you want a system tuned for planets or deep-sky objects. In most cases your telescope and mount will make this choice for you.
  While a deep-sky system can certainly record planets, and a planetary system can image galaxies, the best results almost always come from systems customized for a particular task.
www.sliderbase.com
Notes: The first questions you should ask yourself
What kind of imaging are you interested in doing
The selection of your camera depends strongly on whether you want a system tuned for planets or deep-sky objects. In most cases your telescope and mount will make this choice for you.
While a deep-sky system can certainly record planets, and a planetary system can image galaxies, the best results almost always come from systems customized for a particular task.
The first questions you should ask yourself
What kind of imaging are you interested in doing
The selection of your camera depends strongly on whether you want a system tuned for planets or deep-sky objects. In most cases your telescope and mount will make this choice for you.
While a deep-sky system can certainly record planets, and a planetary system can image galaxies, the best results almost always come from systems customized for a particular task.

## Slide 8: Deep Sky Imaging
  The DEEP-SKY Camera must be:
      Sensitivity
      Low-noise
      Some means of cooling the CCD
        Peltier
        Multi-pinned-phase mode (MPP)
      A large detector (number of pixels verses pixel size)
        600 pixel-square array with 20 micron pixels
        1024 pixel-square array with 10 micron pixels
www.sliderbase.com
Notes: Deep Sky Imaging
The DEEP-SKY Camera must be:
Sensitivity
Low-noise
Some means of cooling the CCD
Peltier
Multi-pinned-phase mode (MPP)
A large detector (number of pixels verses pixel size)
600 pixel-square array with 20 micron pixels
1024 pixel-square array with 10 micron pixels
Deep Sky Imaging
The DEEP-SKY Camera must be:
Sensitivity
Low-noise
Some means of cooling the CCD
Peltier
Multi-pinned-phase mode (MPP)
A large detector (number of pixels verses pixel size)
600 pixel-square array with 20 micron pixels
1024 pixel-square array with 10 micron pixels

## Slide 9: Planetary Imaging
Different rules apply for planetary work
  Dealing with bright objects
  Short exposure times – No cooling required
  Planets can be imaged using very small CCD arrays
    Small arrays have an advantage in that their readout time is more rapid than larger arrays
    Rapid readout facilitates taking many exposures, so you can be selective about which ones you keep
www.sliderbase.com
Notes: Planetary Imaging
Different rules apply for planetary work
Dealing with bright objects
Short exposure times – No cooling required
Planets can be imaged using very small CCD arrays
Small arrays have an advantage in that their readout time is more rapid than larger arrays
Rapid readout facilitates taking many exposures, so you can be selective about which ones you keep
Planetary Imaging
Different rules apply for planetary work
Dealing with bright objects
Short exposure times – No cooling required
Planets can be imaged using very small CCD arrays
Small arrays have an advantage in that their readout time is more rapid than larger arrays
Rapid readout facilitates taking many exposures, so you can be selective about which ones you keep

## Slide 10: CCD Array Sensor
www.sliderbase.com
Notes: CCD Array Sensor
CCD Array Sensor

## Slide 11: Imaging Questions
Why do the stars look square in my images?
Why do my exposures times have to be so long to get any signal?
What is the size of my field of view?
These questions illustrate the three major issues of matching a telescope to a CCD array
    Sampling
    Pixel Sensitivity
    Field of View
www.sliderbase.com
Notes: Imaging Questions
Why do the stars look square in my images?
Why do my exposures times have to be so long to get any signal?
What is the size of my field of view?
These questions illustrate the three major issues of matching a telescope to a CCD array
Sampling
Pixel Sensitivity
Field of View
Imaging Questions
Why do the stars look square in my images?
Why do my exposures times have to be so long to get any signal?
What is the size of my field of view?
These questions illustrate the three major issues of matching a telescope to a CCD array
Sampling
Pixel Sensitivity
Field of View

## Slide 12: Sampling
A CCD image is made up of tiny square-shaped pixels.
Sampling refers to how many pixels are used to produce detail.
Each pixel has a brightness value that is assigned a shade of gray color depending on how many photons strike the pixel during an exposure.
Since pixels are square, the edges of features in an image will have a stair-step appearance.
The more pixels and shades of gray that are used, the smoother the edges will be.
www.sliderbase.com
Notes: Sampling
A CCD image is made up of tiny square-shaped pixels.
Sampling refers to how many pixels are used to produce detail.
Each pixel has a brightness value that is assigned a shade of gray color depending on how many photons strike the pixel during an exposure.
Since pixels are square, the edges of features in an image will have a stair-step appearance.
The more pixels and shades of gray that are used, the smoother the edges will be.
Sampling
A CCD image is made up of tiny square-shaped pixels.
Sampling refers to how many pixels are used to produce detail.
Each pixel has a brightness value that is assigned a shade of gray color depending on how many photons strike the pixel during an exposure.
Since pixels are square, the edges of features in an image will have a stair-step appearance.
The more pixels and shades of gray that are used, the smoother the edges will be.

## Slide 13: Sampling
The following formula can be used to determine sky coverage per pixel with any given pixel size and focal length:
(Sampling in arcseconds) = 206.265 / (focal length in mm) * (pixel size in microns)
Or
(Sampling in arcseconds) = 8.12 / (focal length in inches) * (pixel size in microns)
Undersampled Oversampled
www.sliderbase.com
Notes: Sampling
The following formula can be used to determine sky coverage per pixel with any given pixel size and focal length:
(Sampling in arcseconds) = 206.265 / (focal length in mm) * (pixel size in microns)
Or
(Sampling in arcseconds) = 8.12 / (focal length in inches) * (pixel size in microns)
Undersampled Oversampled
Sampling
The following formula can be used to determine sky coverage per pixel with any given pixel size and focal length:
(Sampling in arcseconds) = 206.265 / (focal length in mm) * (pixel size in microns)
Or
(Sampling in arcseconds) = 8.12 / (focal length in inches) * (pixel size in microns)
Undersampled Oversampled

## Slide 14: Sampling
The CCD user has some control over focal length and pixel size
Average seeing is between 3 to 5 arcseconds
A good rule of thumb to avoid undersampling is to divide your seeing in half and choose a pixel size that provides that amount of sky coverage
www.sliderbase.com
Notes: Sampling
The CCD user has some control over focal length and pixel size
Average seeing is between 3 to 5 arcseconds
A good rule of thumb to avoid undersampling is to divide your seeing in half and choose a pixel size that provides that amount of sky coverage
Sampling
The CCD user has some control over focal length and pixel size
Average seeing is between 3 to 5 arcseconds
A good rule of thumb to avoid undersampling is to divide your seeing in half and choose a pixel size that provides that amount of sky coverage

## Slide 15: Pixel Sensitivity
The larger the pixel, the more sensitive the camera will be for any given focal length.
Under excellent seeing conditions, a camera with 24 micron pixels on a telescope of 2000 mm focal length will produce images that are very close to being undersampled.
For bright planets, oversampling will provide better resolution and it will help cut down the glare that can saturate the CCD pixels.
On the other hand, for faint deepsky objects like galaxies or nebula, moving toward undersampling will give better sensitivity, allowing shorter exposure times.
If an image is to be sharpened, you will get the best results with images that are well sampled.
www.sliderbase.com
Notes: Pixel Sensitivity
The larger the pixel, the more sensitive the camera will be for any given focal length.
Under excellent seeing conditions, a camera with 24 micron pixels on a telescope of 2000 mm focal length will produce images that are very close to being undersampled.
For bright planets, oversampling will provide better resolution and it will help cut down the glare that can saturate the CCD pixels.
On the other hand, for faint deepsky objects like galaxies or nebula, moving toward undersampling will give better sensitivity, allowing shorter exposure times.
If an image is to be sharpened, you will get the best results with images that are well sampled.
Pixel Sensitivity
The larger the pixel, the more sensitive the camera will be for any given focal length.
Under excellent seeing conditions, a camera with 24 micron pixels on a telescope of 2000 mm focal length will produce images that are very close to being undersampled.
For bright planets, oversampling will provide better resolution and it will help cut down the glare that can saturate the CCD pixels.
On the other hand, for faint deepsky objects like galaxies or nebula, moving toward undersampling will give better sensitivity, allowing shorter exposure times.
If an image is to be sharpened, you will get the best results with images that are well sampled.

## Slide 16: Pixel Binning
Most CCDs have the ability to clock multiple pixel charges in both the horizontal and vertical direction into a single larger charge or “super pixel”.
The super pixel represents that area of all individual pixels contributing to the charge.
2x2 binning increase the sensitivity by a factor of 4, but the resolution of the image is cut in half.
www.sliderbase.com
Notes: Pixel Binning
Most CCDs have the ability to clock multiple pixel charges in both the horizontal and vertical direction into a single larger charge or “super pixel”.
The super pixel represents that area of all individual pixels contributing to the charge.
2x2 binning increase the sensitivity by a factor of 4, but the resolution of the image is cut in half.
Pixel Binning
Most CCDs have the ability to clock multiple pixel charges in both the horizontal and vertical direction into a single larger charge or “super pixel”.
The super pixel represents that area of all individual pixels contributing to the charge.
2x2 binning increase the sensitivity by a factor of 4, but the resolution of the image is cut in half.

## Slide 17: Bloomimg vs. Anti-Blooming
www.sliderbase.com
Notes: Bloomimg vs. Anti-Blooming
Bloomimg vs. Anti-Blooming

## Slide 18: Bloomimg vs. Anti-Blooming
www.sliderbase.com
Notes: Bloomimg vs. Anti-Blooming
Bloomimg vs. Anti-Blooming

## Slide 19: Readout Noise
Readout noise is specified both for the CCD sensor and the total system.
First, there is not perfect repeatability each time charge is dumped out of the CCD and digitize.
  Conversions of the same pixel with the same charge will not always yield the same result from the A/D.
The second aspect of noise is the injection of unwanted random signals by the sensor and electronics which ends up getting digitized along with the pixel charge.
Read-out noise is often expressed in the unit known as an electron.
Cameras geared towards amateur astronomy have read noise between 10 and 100 electrons per pixel.
www.sliderbase.com
Notes: Readout Noise
Readout noise is specified both for the CCD sensor and the total system.
First, there is not perfect repeatability each time charge is dumped out of the CCD and digitize.
Conversions of the same pixel with the same charge will not always yield the same result from the A/D.
The second aspect of noise is the injection of unwanted random signals by the sensor and electronics which ends up getting digitized along with the pixel charge.
Read-out noise is often expressed in the unit known as an electron.
Cameras geared towards amateur astronomy have read noise between 10 and 100 electrons per pixel.
Readout Noise
Readout noise is specified both for the CCD sensor and the total system.
First, there is not perfect repeatability each time charge is dumped out of the CCD and digitize.
Conversions of the same pixel with the same charge will not always yield the same result from the A/D.
The second aspect of noise is the injection of unwanted random signals by the sensor and electronics which ends up getting digitized along with the pixel charge.
Read-out noise is often expressed in the unit known as an electron.
Cameras geared towards amateur astronomy have read noise between 10 and 100 electrons per pixel.

## Slide 20: Thermal Noise
Thermal Noise
    The most common term used when describing thermal noise is dark current
    Thermal noise charges, again expressed as electrons, are generated in a CCD camera regardless as to whether it is exposed to light or complete darkness
    Thermal noise is temperature dependent
      The higher the temperature of the CCD the higher the thermal noise
      The lower the temperature of the CCD the lower the thermal noise
      Thermal noise is lowered by decreasing temperature of the CCD. The read out noise stays the same
www.sliderbase.com
Notes: Thermal Noise
Thermal Noise
The most common term used when describing thermal noise is dark current
Thermal noise charges, again expressed as electrons, are generated in a CCD camera regardless as to whether it is exposed to light or complete darkness
Thermal noise is temperature dependent
The higher the temperature of the CCD the higher the thermal noise
The lower the temperature of the CCD the lower the thermal noise
Thermal noise is lowered by decreasing temperature of the CCD. The read out noise stays the same
Thermal Noise
Thermal Noise
The most common term used when describing thermal noise is dark current
Thermal noise charges, again expressed as electrons, are generated in a CCD camera regardless as to whether it is exposed to light or complete darkness
Thermal noise is temperature dependent
The higher the temperature of the CCD the higher the thermal noise
The lower the temperature of the CCD the lower the thermal noise
Thermal noise is lowered by decreasing temperature of the CCD. The read out noise stays the same

## Slide 21: Thermal Noise
www.sliderbase.com
Notes: Thermal Noise
Thermal Noise

## Slide 22: System Gain
System gain is a way of expressing how many electrons of charge are represented by each count (ADU). A gain of 2.5 electrons/ADU indicates that each count or gray level represents 2.5 electrons.
    Kodak KAF-0400=85000/2.5=34000 counts.
As long as the total well depth of a sensor can be represented, a lower gain is better to minimize the noise contribution from the electronics and give better resolution.
Gains which are unnecessarily high can result in more digitization noise, while gains which are too low will minimize noise at the expense of well depth.
    For example, a gain of 1.0 would certainly minimize the electronics contribution to noise, but would only allow 65,536/1.0 = 65,536 electrons of the 85,000 to be digitized.
System gains are designed as a balance between digitization counts, digitization noise, and total well depth.
www.sliderbase.com
Notes: System Gain
System gain is a way of expressing how many electrons of charge are represented by each count (ADU). A gain of 2.5 electrons/ADU indicates that each count or gray level represents 2.5 electrons.
Kodak KAF-0400=85000/2.5=34000 counts.
As long as the total well depth of a sensor can be represented, a lower gain is better to minimize the noise contribution from the electronics and give better resolution.
Gains which are unnecessarily high can result in more digitization noise, while gains which are too low will minimize noise at the expense of well depth.
For example, a gain of 1.0 would certainly minimize the electronics contribution to noise, but would only allow 65,536/1.0 = 65,536 electrons of the 85,000 to be digitized.
System gains are designed as a balance between digitization counts, digitization noise, and total well depth.
System Gain
System gain is a way of expressing how many electrons of charge are represented by each count (ADU). A gain of 2.5 electrons/ADU indicates that each count or gray level represents 2.5 electrons.
Kodak KAF-0400=85000/2.5=34000 counts.
As long as the total well depth of a sensor can be represented, a lower gain is better to minimize the noise contribution from the electronics and give better resolution.
Gains which are unnecessarily high can result in more digitization noise, while gains which are too low will minimize noise at the expense of well depth.
For example, a gain of 1.0 would certainly minimize the electronics contribution to noise, but would only allow 65,536/1.0 = 65,536 electrons of the 85,000 to be digitized.
System gains are designed as a balance between digitization counts, digitization noise, and total well depth.

## Slide 23: Digitization
Digitization, also referred to as analog to digital conversion, is the process by which an analog charge from the CCD is translated into a binary form used by the computer.
The term binary refers to the base 2 number system used.
A 12 bit camera system will output 4096 levels.
A 14 bit system will output 16384 levels.
A 16 bit camera will output 65536 levels.
The higher the digital resolution, the slower the system throughput.
www.sliderbase.com
Notes: Digitization
Digitization, also referred to as analog to digital conversion, is the process by which an analog charge from the CCD is translated into a binary form used by the computer.
The term binary refers to the base 2 number system used.
A 12 bit camera system will output 4096 levels.
A 14 bit system will output 16384 levels.
A 16 bit camera will output 65536 levels.
The higher the digital resolution, the slower the system throughput.
Digitization
Digitization, also referred to as analog to digital conversion, is the process by which an analog charge from the CCD is translated into a binary form used by the computer.
The term binary refers to the base 2 number system used.
A 12 bit camera system will output 4096 levels.
A 14 bit system will output 16384 levels.
A 16 bit camera will output 65536 levels.
The higher the digital resolution, the slower the system throughput.

## Slide 24: Dynamic Range
The dynamic range is often represented as a log ratio of well depth to the readout noise in decibels.
  For example, a system with a well depth of 85,000 electrons and a readout noise of 12 electrons would have a dynamic range = 20 log (85,000/12), or 77dB. The higher the number the better.
This ratio also gives an indication of the number of digitization levels that might be appropriate for a given sensor. A sensor with a well depth of 35,000 electrons and with 15 electrons of read noise would yield a ratio of 35,000/15=2333. Unless there is a desire to resolve this noise with a 16 bit system into 65,536 gray shades, a 12 bit system with 4096 levels would be more than adequate for this sensor.
www.sliderbase.com
Notes: Dynamic Range
The dynamic range is often represented as a log ratio of well depth to the readout noise in decibels.
For example, a system with a well depth of 85,000 electrons and a readout noise of 12 electrons would have a dynamic range = 20 log (85,000/12), or 77dB. The higher the number the better.
This ratio also gives an indication of the number of digitization levels that might be appropriate for a given sensor. A sensor with a well depth of 35,000 electrons and with 15 electrons of read noise would yield a ratio of 35,000/15=2333. Unless there is a desire to resolve this noise with a 16 bit system into 65,536 gray shades, a 12 bit system with 4096 levels would be more than adequate for this sensor.
Dynamic Range
The dynamic range is often represented as a log ratio of well depth to the readout noise in decibels.
For example, a system with a well depth of 85,000 electrons and a readout noise of 12 electrons would have a dynamic range = 20 log (85,000/12), or 77dB. The higher the number the better.
This ratio also gives an indication of the number of digitization levels that might be appropriate for a given sensor. A sensor with a well depth of 35,000 electrons and with 15 electrons of read noise would yield a ratio of 35,000/15=2333. Unless there is a desire to resolve this noise with a 16 bit system into 65,536 gray shades, a 12 bit system with 4096 levels would be more than adequate for this sensor.

## Slide 25: Quantum Efficiency
The quantum efficiency (Q.E.) of a sensor describes its response to different wavelengths of light
www.sliderbase.com
Notes: Quantum Efficiency
The quantum efficiency (Q.E.) of a sensor describes its response to different wavelengths of light
Quantum Efficiency
The quantum efficiency (Q.E.) of a sensor describes its response to different wavelengths of light

## Slide 26: Charge Transfer Efficiency
As each charge is transferred, not every electron will be carried along with perfect efficiency. Some get "left behind" or trapped.
Charge Transfer Efficiency of 0.99997 can be thought of as 2.5 electrons out of 85,000 electrons not transferred or "lost in the shuffle".
Since the CTE is sensor dependent, all manufacturers of imaging systems using the same sensor will start with the same efficiency specification. Improper camera system design can cause less than optimum charge transfer efficiency.
www.sliderbase.com
Notes: Charge Transfer Efficiency
As each charge is transferred, not every electron will be carried along with perfect efficiency. Some get "left behind" or trapped.
Charge Transfer Efficiency of 0.99997 can be thought of as 2.5 electrons out of 85,000 electrons not transferred or "lost in the shuffle".
Since the CTE is sensor dependent, all manufacturers of imaging systems using the same sensor will start with the same efficiency specification. Improper camera system design can cause less than optimum charge transfer efficiency.
Charge Transfer Efficiency
As each charge is transferred, not every electron will be carried along with perfect efficiency. Some get "left behind" or trapped.
Charge Transfer Efficiency of 0.99997 can be thought of as 2.5 electrons out of 85,000 electrons not transferred or "lost in the shuffle".
Since the CTE is sensor dependent, all manufacturers of imaging systems using the same sensor will start with the same efficiency specification. Improper camera system design can cause less than optimum charge transfer efficiency.

## Slide 27: Data Rate and Transfer Rate
The key consideration here is, "How long from the time the shutter closes do I have to wait to see the image?"
The shorter this time is, the easier to focus the system and more enjoyable the CCD imaging experience will be.
Also, dark count continues to build during the delay and readout. The longer the actual charge transfer time from the CCD, the greater the top to bottom dark count gradient.
www.sliderbase.com
Notes: Data Rate and Transfer Rate
The key consideration here is, "How long from the time the shutter closes do I have to wait to see the image?"
The shorter this time is, the easier to focus the system and more enjoyable the CCD imaging experience will be.
Also, dark count continues to build during the delay and readout. The longer the actual charge transfer time from the CCD, the greater the top to bottom dark count gradient.
Data Rate and Transfer Rate
The key consideration here is, "How long from the time the shutter closes do I have to wait to see the image?"
The shorter this time is, the easier to focus the system and more enjoyable the CCD imaging experience will be.
Also, dark count continues to build during the delay and readout. The longer the actual charge transfer time from the CCD, the greater the top to bottom dark count gradient.

## Slide 28: Correlated Double Sampling
Virtually all serious imaging systems employ this technique in various manners.
Correlated double sampling yields the best representation of the true charge associated with each pixel.
www.sliderbase.com
Notes: Correlated Double Sampling
Virtually all serious imaging systems employ this technique in various manners.
Correlated double sampling yields the best representation of the true charge associated with each pixel.
Correlated Double Sampling
Virtually all serious imaging systems employ this technique in various manners.
Correlated double sampling yields the best representation of the true charge associated with each pixel.

## Slide 29: Other Factors
Weight
Electronics Modules
    Surface mount technology
    Stay away from cameras with bulky external control boxes
Number of camera connections
Camera start-up procedures
    Peltier Cooler
      Starlight Xpress – just plug in he camera
      SBIG – Controlled by software
    Cooling Fans
      Can induce vibrations
www.sliderbase.com
Notes: Other Factors
Weight
Electronics Modules
Surface mount technology
Stay away from cameras with bulky external control boxes
Number of camera connections
Camera start-up procedures
Peltier Cooler
Starlight Xpress – just plug in he camera
SBIG – Controlled by software
Cooling Fans
Can induce vibrations
Other Factors
Weight
Electronics Modules
Surface mount technology
Stay away from cameras with bulky external control boxes
Number of camera connections
Camera start-up procedures
Peltier Cooler
Starlight Xpress – just plug in he camera
SBIG – Controlled by software
Cooling Fans
Can induce vibrations

## Slide 30: Other Factors
Is the software user friendly
    Drop-down menus
    Dialog boxes
    Keyboard shortcuts
Learning curve of the camera
    Large instruction manuals
      Using your camera should be an enjoyable experience
www.sliderbase.com
Notes: Other Factors
Is the software user friendly
Drop-down menus
Dialog boxes
Keyboard shortcuts
Learning curve of the camera
Large instruction manuals
Using your camera should be an enjoyable experience
Other Factors
Is the software user friendly
Drop-down menus
Dialog boxes
Keyboard shortcuts
Learning curve of the camera
Large instruction manuals
Using your camera should be an enjoyable experience

## Slide 31: Basic Imaging Concepts
www.sliderbase.com
Notes: Basic Imaging Concepts
Basic Imaging Concepts

## Slide 32: More “Buzz” Words
Bias Frames
Light Boxes
T-Shirt Flats
Flat Fields
Dark Frames
Raw Imagines
Calibrated Image
Signal vs. Noise
www.sliderbase.com
Notes: More “Buzz” Words
Bias Frames
Light Boxes
T-Shirt Flats
Flat Fields
Dark Frames
Raw Imagines
Calibrated Image
Signal vs. Noise
More “Buzz” Words
Bias Frames
Light Boxes
T-Shirt Flats
Flat Fields
Dark Frames
Raw Imagines
Calibrated Image
Signal vs. Noise

## Slide 33: Bias Frames
Astronomers make bias frames to capture the bias level.
Bias frames represent noise levels that occur on a CCD detector when placed in total darkness with an integration time of zero.
These frames represent the minimum noise generated by the camera electronics as pixel values are read from the CCD array.
This bias level can fluctuate because of things that happen every time the CCD is read out or because extraneous signals are added to the bias level. These un-patterned events can originate in power supplies, nearby electronics, motors, and radio-frequency interference from computers and monitors.
The noise in these bias frames is extremely low; so many CCD imagers do not bother to apply them to their images.
www.sliderbase.com
Notes: Bias Frames
Astronomers make bias frames to capture the bias level.
Bias frames represent noise levels that occur on a CCD detector when placed in total darkness with an integration time of zero.
These frames represent the minimum noise generated by the camera electronics as pixel values are read from the CCD array.
This bias level can fluctuate because of things that happen every time the CCD is read out or because extraneous signals are added to the bias level. These un-patterned events can originate in power supplies, nearby electronics, motors, and radio-frequency interference from computers and monitors.
The noise in these bias frames is extremely low; so many CCD imagers do not bother to apply them to their images.
Bias Frames
Astronomers make bias frames to capture the bias level.
Bias frames represent noise levels that occur on a CCD detector when placed in total darkness with an integration time of zero.
These frames represent the minimum noise generated by the camera electronics as pixel values are read from the CCD array.
This bias level can fluctuate because of things that happen every time the CCD is read out or because extraneous signals are added to the bias level. These un-patterned events can originate in power supplies, nearby electronics, motors, and radio-frequency interference from computers and monitors.
The noise in these bias frames is extremely low; so many CCD imagers do not bother to apply them to their images.

## Slide 34: Why take Bias Frames?
They give you a history of your cameras operational functionally.
Noise level changes
Interference
They are needed if you intend to do astrometry, photometry or to get the best results from your images.
NOTE: SBIG cameras add a 100-unit pedestal to each Bias, Dark, Flat-
Field, and Light frame. This pedestal value is subtracted by
CCDSoft during the data reduction process. This will need to be
subtracted manually with other IP programs.
www.sliderbase.com
Notes: Why take Bias Frames?
They give you a history of your cameras operational functionally.
Noise level changes
Interference
They are needed if you intend to do astrometry, photometry or to get the best results from your images.
NOTE: SBIG cameras add a 100-unit pedestal to each Bias, Dark, Flat-
Field, and Light frame. This pedestal value is subtracted by
CCDSoft during the data reduction process. This will need to be
subtracted manually with other IP programs.
Why take Bias Frames?
They give you a history of your cameras operational functionally.
Noise level changes
Interference
They are needed if you intend to do astrometry, photometry or to get the best results from your images.
NOTE: SBIG cameras add a 100-unit pedestal to each Bias, Dark, Flat-
Field, and Light frame. This pedestal value is subtracted by
CCDSoft during the data reduction process. This will need to be
subtracted manually with other IP programs.

## Slide 35: Bias Frame Demo Read Out Noise Demo
www.sliderbase.com
Notes: Bias Frame Demo Read Out Noise Demo
Bias Frame Demo Read Out Noise Demo

## Slide 36: Dark Frames
Even when a CCD array is placed in total darkness, individual pixels build up a charge over time. Most of this noise is generated by heat, and is called thermal noise or dark current. Lowering the temperature of the CCD array can reduce this thermal noise. The colder you can make the array, the lower the thermal noise.
www.sliderbase.com
Notes: Dark Frames
Even when a CCD array is placed in total darkness, individual pixels build up a charge over time. Most of this noise is generated by heat, and is called thermal noise or dark current. Lowering the temperature of the CCD array can reduce this thermal noise. The colder you can make the array, the lower the thermal noise.
Dark Frames
Even when a CCD array is placed in total darkness, individual pixels build up a charge over time. Most of this noise is generated by heat, and is called thermal noise or dark current. Lowering the temperature of the CCD array can reduce this thermal noise. The colder you can make the array, the lower the thermal noise.

## Slide 37: Dark Frames
www.sliderbase.com
Notes: Dark Frames
Dark Frames

## Slide 38: Cosmic Rays
www.sliderbase.com
Notes: Cosmic Rays
Cosmic Rays

## Slide 39: Flat Fields
Taking an image of an evenly illuminated surface will create a flat field frame. Even though the CCD detector has been exposed to an evenly illuminated surface, the charge built up on each pixel can vary; flat fields are used to correct for these variations. There are other circumstances, which can help create these variations such as internal reflections, central obstructions and dust on optical surfaces.
NOTE: CCD detectors and their electronics have natural variations in the full-well depth and gain settings so the average value of the brightest area in a flat field should fall between 33% and 50% of the CCD’s saturation point.
www.sliderbase.com
Notes: Flat Fields
Taking an image of an evenly illuminated surface will create a flat field frame. Even though the CCD detector has been exposed to an evenly illuminated surface, the charge built up on each pixel can vary; flat fields are used to correct for these variations. There are other circumstances, which can help create these variations such as internal reflections, central obstructions and dust on optical surfaces.
NOTE: CCD detectors and their electronics have natural variations in the full-well depth and gain settings so the average value of the brightest area in a flat field should fall between 33% and 50% of the CCD’s saturation point.
Flat Fields
Taking an image of an evenly illuminated surface will create a flat field frame. Even though the CCD detector has been exposed to an evenly illuminated surface, the charge built up on each pixel can vary; flat fields are used to correct for these variations. There are other circumstances, which can help create these variations such as internal reflections, central obstructions and dust on optical surfaces.
NOTE: CCD detectors and their electronics have natural variations in the full-well depth and gain settings so the average value of the brightest area in a flat field should fall between 33% and 50% of the CCD’s saturation point.

## Slide 40: How do you find the saturation point?
Full Well Capacity / Gain = The Saturation Point
For the ST-7E ABG
50,000 / 2.3 = 21,740
21,740 * .33 = 7,250 21,740 * .50 = 11,000
www.sliderbase.com
Notes: How do you find the saturation point?
Full Well Capacity / Gain = The Saturation Point
For the ST-7E ABG
50,000 / 2.3 = 21,740
21,740 * .33 = 7,250 21,740 * .50 = 11,000
How do you find the saturation point?
Full Well Capacity / Gain = The Saturation Point
For the ST-7E ABG
50,000 / 2.3 = 21,740
21,740 * .33 = 7,250 21,740 * .50 = 11,000

## Slide 41: Flat Fields
www.sliderbase.com
Notes: Flat Fields
Flat Fields

## Slide 42: Flat Field Demo
www.sliderbase.com
Notes: Flat Field Demo
Flat Field Demo

## Slide 43: Reduction of Dark and Flat Fields
www.sliderbase.com
Notes: Reduction of Dark and Flat Fields
Reduction of Dark and Flat Fields

## Slide 44: Dark Frame Subtraction Demo
www.sliderbase.com
Notes: Dark Frame Subtraction Demo
Dark Frame Subtraction Demo

## Slide 45: Spatial Filtering
Spatial filtering is widely used to extract detail and control noise. This filtering modifies a pixel according to the appearance of its neighbors.
Low-Pass Filtering
  Sometimes called blurring or smoothing, low-pass filtering averages out rapid changes of intensity from one pixel to the next.
  Why would you what to blur or smooth an image?
    To suppress noise.
www.sliderbase.com
Notes: Spatial Filtering
Spatial filtering is widely used to extract detail and control noise. This filtering modifies a pixel according to the appearance of its neighbors.
Low-Pass Filtering
Sometimes called blurring or smoothing, low-pass filtering averages out rapid changes of intensity from one pixel to the next.
Why would you what to blur or smooth an image?
To suppress noise.
Spatial Filtering
Spatial filtering is widely used to extract detail and control noise. This filtering modifies a pixel according to the appearance of its neighbors.
Low-Pass Filtering
Sometimes called blurring or smoothing, low-pass filtering averages out rapid changes of intensity from one pixel to the next.
Why would you what to blur or smooth an image?
To suppress noise.

## Slide 46: Convolution Kernel
www.sliderbase.com
Notes: Convolution Kernel
Convolution Kernel

## Slide 47: Convolution Matrix
The intensity of the image point located at the center of the matrix is replaced by the weighted average intensity of all the point located inside the matrix.
P1 P2 P3
P4 P5 P6
P7 P8 P9
P5 = (P1 + 2 * P2 + P3 + 2 * P4 + 4 * P5 + 2 * P6 + P7 + 2 * P8 + P9) / 16
The convoluted image is divided by the sum of the weighting coefficients: 16, 6, 8, and 2 respectively.
www.sliderbase.com
Notes: Convolution Matrix
The intensity of the image point located at the center of the matrix is replaced by the weighted average intensity of all the point located inside the matrix.
P1 P2 P3
P4 P5 P6
P7 P8 P9
P5 = (P1 + 2 * P2 + P3 + 2 * P4 + 4 * P5 + 2 * P6 + P7 + 2 * P8 + P9) / 16
The convoluted image is divided by the sum of the weighting coefficients: 16, 6, 8, and 2 respectively.
Convolution Matrix
The intensity of the image point located at the center of the matrix is replaced by the weighted average intensity of all the point located inside the matrix.
P1 P2 P3
P4 P5 P6
P7 P8 P9
P5 = (P1 + 2 * P2 + P3 + 2 * P4 + 4 * P5 + 2 * P6 + P7 + 2 * P8 + P9) / 16
The convoluted image is divided by the sum of the weighting coefficients: 16, 6, 8, and 2 respectively.

## Slide 48: Median Filter
A variation on low-pass filtering and is better at eliminating noise.
Instead of replacing a pixel with the average of its neighbors, it is replaced with the median within the ensemble.
This filter is good for removing “hot” and “cold” pixels from an image.
www.sliderbase.com
Notes: Median Filter
A variation on low-pass filtering and is better at eliminating noise.
Instead of replacing a pixel with the average of its neighbors, it is replaced with the median within the ensemble.
This filter is good for removing “hot” and “cold” pixels from an image.
Median Filter
A variation on low-pass filtering and is better at eliminating noise.
Instead of replacing a pixel with the average of its neighbors, it is replaced with the median within the ensemble.
This filter is good for removing “hot” and “cold” pixels from an image.

## Slide 49: High-Pass
A high-pass filter emphasizes fine detail in an image – exactly the opposite of what a low-pass filter does.
High-pass filters work exactly the same way, except that they use a different kernel.
High-pass filters can sharpen an image blurred by atmospheric seeing or poor focus.
Unfortunately, their effect on noise is also the opposite of a low-pass filter; noise becomes amplified.
www.sliderbase.com
Notes: High-Pass
A high-pass filter emphasizes fine detail in an image – exactly the opposite of what a low-pass filter does.
High-pass filters work exactly the same way, except that they use a different kernel.
High-pass filters can sharpen an image blurred by atmospheric seeing or poor focus.
Unfortunately, their effect on noise is also the opposite of a low-pass filter; noise becomes amplified.
High-Pass
A high-pass filter emphasizes fine detail in an image – exactly the opposite of what a low-pass filter does.
High-pass filters work exactly the same way, except that they use a different kernel.
High-pass filters can sharpen an image blurred by atmospheric seeing or poor focus.
Unfortunately, their effect on noise is also the opposite of a low-pass filter; noise becomes amplified.

## Slide 50: Unsharp Masking
Unsharp masking is a variation of the high-pass filtering.
A low pass filter is first used to make a blurry copy of the original images.
This copy is subtracted from the original, suppressing large-scale features and leaving fine detail.
Unsharp masking is very effective for planetary imaging
Do not overdo high-pass filtering, since small, faint details can be greatly exaggerated. The result might not be a realistic view of the object.
An over processed image will look grainy and unnatural.
www.sliderbase.com
Notes: Unsharp Masking
Unsharp masking is a variation of the high-pass filtering.
A low pass filter is first used to make a blurry copy of the original images.
This copy is subtracted from the original, suppressing large-scale features and leaving fine detail.
Unsharp masking is very effective for planetary imaging
Do not overdo high-pass filtering, since small, faint details can be greatly exaggerated. The result might not be a realistic view of the object.
An over processed image will look grainy and unnatural.
Unsharp Masking
Unsharp masking is a variation of the high-pass filtering.
A low pass filter is first used to make a blurry copy of the original images.
This copy is subtracted from the original, suppressing large-scale features and leaving fine detail.
Unsharp masking is very effective for planetary imaging
Do not overdo high-pass filtering, since small, faint details can be greatly exaggerated. The result might not be a realistic view of the object.
An over processed image will look grainy and unnatural.

## Slide 51: Deconvolution
Once we filter an image, we can undo the results through a process called deconvolution.
With deconvolution,instead of multiplying pixel data by a filter, we divide it.
Deconvolution can reduce the effects of atmospheric seeing and even defects created by poor optics.
www.sliderbase.com
Notes: Deconvolution
Once we filter an image, we can undo the results through a process called deconvolution.
With deconvolution,instead of multiplying pixel data by a filter, we divide it.
Deconvolution can reduce the effects of atmospheric seeing and even defects created by poor optics.
Deconvolution
Once we filter an image, we can undo the results through a process called deconvolution.
With deconvolution,instead of multiplying pixel data by a filter, we divide it.
Deconvolution can reduce the effects of atmospheric seeing and even defects created by poor optics.

## Slide 52: Spatial Filtering Summary
Here are some guidelines I’ve found useful:
  Low-pass filtering is good for picking faint nebulosity out of noisy images.
  High-pass filtering and unsharp masking works well on lunar and planetary images.
  Median filtering is good for reducing the noise in an image, particularly hot and cold pixels.
  Deconvolution works well on high-resolution images.
  After passing an image through a filtering algorithm, try processing it with a stretching function.
www.sliderbase.com
Notes: Spatial Filtering Summary
Here are some guidelines I’ve found useful:
Low-pass filtering is good for picking faint nebulosity out of noisy images.
High-pass filtering and unsharp masking works well on lunar and planetary images.
Median filtering is good for reducing the noise in an image, particularly hot and cold pixels.
Deconvolution works well on high-resolution images.
After passing an image through a filtering algorithm, try processing it with a stretching function.
Spatial Filtering Summary
Here are some guidelines I’ve found useful:
Low-pass filtering is good for picking faint nebulosity out of noisy images.
High-pass filtering and unsharp masking works well on lunar and planetary images.
Median filtering is good for reducing the noise in an image, particularly hot and cold pixels.
Deconvolution works well on high-resolution images.
After passing an image through a filtering algorithm, try processing it with a stretching function.

## Slide 53: The Importance of Average Stacking
Averaging reduces noise by the square root of the number of frames you average.
  4 images = noise reduced by a factor of ½
  9 images = noise reduced by a factor of 3
  20 images = noise reduced by a factor of 4.5
1 image 3 images 10 images
www.sliderbase.com
Notes: The Importance of Average Stacking
Averaging reduces noise by the square root of the number of frames you average.
4 images = noise reduced by a factor of ½
9 images = noise reduced by a factor of 3
20 images = noise reduced by a factor of 4.5
1 image 3 images 10 images
The Importance of Average Stacking
Averaging reduces noise by the square root of the number of frames you average.
4 images = noise reduced by a factor of ½
9 images = noise reduced by a factor of 3
20 images = noise reduced by a factor of 4.5
1 image 3 images 10 images

## Slide 54: Image Stacking Demo
www.sliderbase.com
Notes: Image Stacking Demo
Image Stacking Demo

## Slide 55: Mosaic Demo
www.sliderbase.com
Notes: Mosaic Demo
Mosaic Demo

## Slide 56: Images
www.sliderbase.com
Notes: Images
Images

## Slide 57: Images
www.sliderbase.com
Notes: Images
Images

## Slide 58: Images
www.sliderbase.com
Notes: Images
Images

## Slide 59: Asteroid Data Screen
www.sliderbase.com
Notes: Asteroid Data Screen
Asteroid Data Screen

## Slide 60: Quick Charts
www.sliderbase.com
Notes: Quick Charts
Quick Charts

## Slide 61: Ephemeris Generator
www.sliderbase.com
Notes: Ephemeris Generator
Ephemeris Generator

## Slide 62: Calendar Screen
www.sliderbase.com
Notes: Calendar Screen
Calendar Screen

## Slide 63: Measure Screen
www.sliderbase.com
Notes: Measure Screen
Measure Screen

## Slide 64: Charting Information
www.sliderbase.com
Notes: Charting Information
Charting Information

## Slide 65: Photometry Data
www.sliderbase.com
Notes: Photometry Data
Photometry Data

## Slide 66: Calculated Measurement Screen
www.sliderbase.com
Notes: Calculated Measurement Screen
Calculated Measurement Screen

## Slide 67: Reporting Screen
www.sliderbase.com
Notes: Reporting Screen
Reporting Screen

## Slide 68: Data
www.sliderbase.com
Notes: Data
Data

## Slide 69: Questions?
www.sliderbase.com
Notes: Questions?
Questions?