## Slide 1: Definition of Radiation
“Radiation is an energy in the form of electro-magnetic waves or particulate matter, traveling in the air.”
www.sliderbase.com

## Slide 2
Forces: There are many interactions among nuclei. It turns out that there are forces other than the electromagnetic force and the gravitational force which govern the interactions among nuclei.
Einstein in 1905m showed 2 more laws: energy/mass, and binding energy
www.sliderbase.com

## Slide 3
Radioactivity: Elements & Atoms
Atoms are composed of smaller particles referred to as:
  Protons
  Neutrons
  Electrons
www.sliderbase.com

## Slide 4: Basic Model of a Neutral Atom.
Electrons (-) orbiting nucleus of protons (+) and neutrons. Same number of electrons as protons; net charge = 0.
Atomic number (number of protons) determines element.
Mass number (protons + neutrons)
www.sliderbase.com

## Slide 5
www.sliderbase.com

## Slide 6: Radioactivity
If a nucleus is unstable for any reason, it will emit and absorb particles. There are many types of radiation and they are all pertinent to everyday life and health as well as nuclear physical applications.
www.sliderbase.com

## Slide 7
Ionization
Ionizing radiation is produced by unstable atoms. Unstable atoms differ from stable atoms because they have an excess of energy or mass or both.
Unstable atoms are said to be radioactive. In order to reach stability, these atoms give off, or emit, the excess energy or mass. These emissions are called radiation.
www.sliderbase.com

## Slide 8
www.sliderbase.com

## Slide 9
www.sliderbase.com

## Slide 10
www.sliderbase.com

## Slide 11
www.sliderbase.com

## Slide 12
Types or Products of Ionizing Radiation


or X-ray
neutron
www.sliderbase.com

## Slide 13
Ionizing Radiation
alpha particle
beta particle
Radioactive Atom
X-ray
gamma ray
www.sliderbase.com

## Slide 14
The electro-magnetic waves vary in their length and frequency along a very wide spectrum.
www.sliderbase.com

## Slide 15
www.sliderbase.com

## Slide 16
www.sliderbase.com

## Slide 17
www.sliderbase.com

## Slide 18: Types of Radiation
Radiation is classified into:
  Ionizing radiation
  Non-ionizing radiation
www.sliderbase.com

## Slide 19
Ionizing Versus Non-ionizing Radiation
Ionizing Radiation
  Higher energy electromagnetic waves (gamma) or heavy particles (beta and alpha).
  High enough energy to pull electron from orbit.
Non-ionizing Radiation
  Lower energy electromagnetic waves.
  Not enough energy to pull electron from orbit, but can excite the electron.
www.sliderbase.com

## Slide 20: Ionizing Radiation
Definition:
“ It is a type of radiation that is able to disrupt atoms and molecules on which they pass through, giving rise to ions and free radicals”.
www.sliderbase.com

## Slide 21: Another Definition
Ionizing radiation
A radiation is said to be ionizing when it has enough energy to eject one or more electrons from the atoms or molecules in the irradiated medium. This is the case of a and b radiations, as well as of electromagnetic radiations such as gamma radiations, X-rays and some ultra-violet rays. Visible or infrared light are not, nor are microwaves or radio waves.
www.sliderbase.com

## Slide 22
Primary Types of Ionizing Radiation
Alpha particles
Beta particles
Gamma rays (or photons)
X-Rays (or photons)
Neutrons
www.sliderbase.com

## Slide 23
Alpha Particles: 2 neutrons and 2 protons
They travel short distances, have large mass
Only a hazard when inhaled
Types and Characteristics of Ionizing Radiation Alpha Particles
www.sliderbase.com

## Slide 24
Alpha Particles (or Alpha Radiation): Helium nucleus (2 neutrons and 2 protons); +2 charge; heavy (4 AMU). Typical Energy = 4-8 MeV; Limited range (<10cm in air; 60µm in tissue); High LET (QF=20) causing heavy damage (4K-9K ion pairs/µm in tissue). Easily shielded (e.g., paper, skin) so an internal radiation hazard. Eventually lose too much energy to ionize; become He.
www.sliderbase.com

## Slide 25
Beta Particles
Beta Particles: Electrons or positrons having small mass and variable energy. Electrons form when a neutron transforms into a proton and an electron or:
www.sliderbase.com

## Slide 26
Beta Particles: High speed electron ejected from nucleus; -1 charge, light 0.00055 AMU; Typical Energy = several KeV to 5 MeV; Range approx. 12'/MeV in air, a few mm in tissue; Low LET (QF=1) causing light damage (6-8 ion pairs/µm in tissue). Primarily an internal hazard, but high beta can be an external hazard to skin. In addition, the high speed electrons may lose energy in the form of X-rays when they quickly decelerate upon striking a heavy material. This is called Bremsstralung (or Breaking) Radiation. Aluminum and other light (<14) materials are used for shielding.
www.sliderbase.com

## Slide 27
www.sliderbase.com

## Slide 28
Gamma Rays
Gamma Rays (or photons): Result when the nucleus releases energy, usually after an alpha, beta or positron transition
www.sliderbase.com

## Slide 29
X-Rays
X-Rays: Occur whenever an inner shell orbital electron is removed and rearrangement of the atomic electrons results with the release of the elements characteristic X-Ray energy
www.sliderbase.com

## Slide 30
X- and Gamma Rays: X-rays are photons (Electromagnetic radiations) emitted from electron orbits. Gamma rays are photons emitted from the nucleus, often as part of radioactive decay. Gamma rays typically have higher energy (Mev's) than X-rays (KeV's), but both are unlimited.
www.sliderbase.com

## Slide 31
Neutrons
Neutrons: Have the same mass as protons but are uncharged
www.sliderbase.com

## Slide 32
www.sliderbase.com

## Slide 33
www.sliderbase.com

## Slide 34: QUANTIFICATION OF RADIATION
A. Quantifying Radioactive Decay
B. Quantifying Exposure and Dose
www.sliderbase.com

## Slide 35: A. Quantifying Radioactive Decay
Measurement of Activity in disintegrations per second (dps);
1 Becquerel (Bq) = 1 dps;
1 Curie (Ci) = 3.7 x 1010 dps;
Activity of substances are expressed as activity per weight or volume (e.g., Bq/gm or Ci/l).
www.sliderbase.com

## Slide 36: B. Quantifying Exposure and Dose
Exposure: Roentgen 1 Roentgen (R) = amount of X or gamma radiation that produces ionization resulting in 1 electrostatic unit of charge in 1 cm3 of dry air. Instruments often measure exposure rate in mR/hr.
Absorbed Dose: rad (Roentgen absorbed dose) = absorption of 100 ergs of energy from any radiation in 1 gram of any material; 1 Gray (Gy) = 100 rads = 1 Joule/kg; Exposure to 1 Roentgen approximates 0.9 rad in air.
Biologically Equivalent Dose: Rem (Roentgen equivalent man) = dose in rads x QF, where QF = quality factor. 1 Sievert (Sv) = 100 rems.
www.sliderbase.com

## Slide 37
Half Life Calculation
www.sliderbase.com

## Slide 38
Ionizing Radiation at the Cellular Level
Causes breaks in one or both DNA strands or;
Causes Free Radical formation
www.sliderbase.com

## Slide 39: Exposure Limits
OSHA Limits: Whole body limit = 1.25 rem/qtr or 5 rem (50 mSv) per year.
Hands and feet limit = 18.75 rem/qtr.
Skin of whole body limit = 7.5 rem/qtr.
Total life accumulation = 5 x (N-18) rem where N = age. Can have 3 rem/qtr if total life accumulation not exceeded.
Note: New recommendations reduce the 5 rem to 2 rem.
www.sliderbase.com

## Slide 40
External/Internal Exposure Limits for Occupationally Exposed Individuals
Annual Dose Limits
Adult (>18 yrs)
Minor (< 18 yrs)
Whole body*
5000 mrem/yr
500 mrem/yr
Lens of eye
15000 mrem/yr
1500 mrem/yr
Extremities
50000 mrem/yr
5000 mrem/yr
Skin
50000 mrem/yr
5000 mrem/yr
Organ
50000 mrem/yr
5000 mrem/yr
        *Effective dose equivalent
www.sliderbase.com

## Slide 41
www.sliderbase.com

## Slide 42: Community Emergency Radiation
Hazardous Waste Sites:
Radiation above background (0.01-0.02 m rem/hr) signifies possible presence which must be monitored. Radiation above 2 m rem/hr indicates potential hazard. Evacuate site until controlled.
www.sliderbase.com

## Slide 43
Your Annual Exposure
Activity
Typical Dose
Smoking
280 millirem/year
Radioactive materials use in a UM lab
<10 millirem/year
Dental x-ray
10 millirem per x-ray
Chest x-ray
8 millirem per x-ray
Drinking water
5 millirem/year
Cross country round trip by air
5 millirem per trip
Coal Burning power plant
0.165 millirem/year
www.sliderbase.com

## Slide 44
HEALTH EFFECTS
Generalizations: Biological effects are due to the ionization process that destroys the capacity for cell reproduction or division or causes cell mutation. A given total dose will cause more damage if received in a shorter time period. A fatal dose is (600 R)
Acute Somatic Effects: Relatively immediate effects to a person acutely exposed. Severity depends on dose. Death usually results from damage to bone marrow or intestinal wall. Acute radio-dermatitis is common in radiotherapy; chronic cases occur mostly in industry.
www.sliderbase.com

## Slide 45
0-25 | No observable effect.
25-50 | Minor temporary blood changes.
50-100 | Possible nausea and vomiting and reduced WBC.
150-300 | Increased severity of above and diarrhea, malaise, loss of appetite.
300-500 | Increased severity of above and hemorrhaging, depilation. Death may occur
> 500 | Symptoms appear immediately, then death has to occur.
ACUTE DOSE(RAD) EFFECT
www.sliderbase.com

## Slide 46
Delayed Somatic Effects: Delayed effects to exposed person include: Cancer, leukemia, cataracts, life shortening from organ failure, and abortion. Probability of an effect is proportional to dose (no threshold). Severity is independent of dose. Doubling dose for cancer is approximately 10-100 rems.
Genetic Effects: Genetic effects to off-spring of exposed persons are irreversible and nearly always harmful. Doubling dose for mutation rate is approximately 50-80 rems. (Spontaneous mutation rate is approx. 10-100 mutations per million population per generation.)
www.sliderbase.com

## Slide 47
Critical Organs: Organs generally most susceptible to radiation damage include: Lymphocytes, bone marrow, gastro-intestinal, gonads, and other fast-growing cells. The central nervous system is relatively resistant. Many nuclides concentrate in certain organs rather than being uniformly distributed over the body, and the organs may be particularly sensitive to radiation damage, e.g., isotopes of iodine concentrate in the thyroid gland. These organs are considered "critical" for the specific nuclide.
www.sliderbase.com

## Slide 48: Non-ionizing Radiation
Definition:
“ They are electromagnetic waves incapable of producing ions while passing through matter, due to their lower energy.”
www.sliderbase.com

## Slide 49
  All earth surface system components emit radiation---the sun and the earth are the components we are most interested in
  The sun emits radiation composed of high energy infrared radiation, visible light, and ultraviolet radiation collectively known as shortwave radiation (SW)
  The earth emits radiation composed of lower energy infrared radiation collectively known as long-wave radiation (LW)
www.sliderbase.com

## Slide 50
www.sliderbase.com

## Slide 51
Path of incoming solar radiation
www.sliderbase.com

## Slide 52
Albedo: a measure of how well a surface reflects insolation
www.sliderbase.com

## Slide 53
Examples on Non-ionizing Radiation Sources
Visible light
Microwaves
Radios
Video Display Terminals
Power lines
Radiofrequency Diathermy (Physical Therapy)
Lasers
MICROWAVE
GAMMA
ULTRA V
VISIBLE
INFRARED
TV
AM
RF
www.sliderbase.com

## Slide 54: Other Manmade Sources of Non-Ionizing Radiation
www.sliderbase.com

## Slide 55
www.sliderbase.com

## Slide 56
www.sliderbase.com

## Slide 57: Effects
Radiofrequency Ranges (10 kHz to 300 GHz)
  Effects only possible at ten times the permissible exposure limit
  Heating of the body (thermal effect)
  Cataracts
  Some studies show effects of teratoginicity and carcinogenicity.
www.sliderbase.com

## Slide 58: RADIATION CONTROLS
A. Basic Control Methods for External Radiation
Decrease Time
Increase Distance
Increase Shielding
www.sliderbase.com

## Slide 59
Time: Minimize time of exposure to minimize total dose. Rotate employees to restrict individual dose.
Distance: Maximize distance to source to maximize attenuation in air. The effect of distance can be estimated from equations.
Shielding: Minimize exposure by placing absorbing shield between worker and source.
www.sliderbase.com

## Slide 60
www.sliderbase.com

## Slide 61: B. Monitoring
Personal Dosimeters: Normally they do not prevent exposures (no alarm), just record it. They can provide a record of accumulated exposure for an individual worker over extended periods of time (hours, days or weeks), and are small enough for measuring localized exposures Common types: Film badges; Thermoluminescence detectors (TLD); and pocket dosimeters.
www.sliderbase.com

## Slide 62
www.sliderbase.com

## Slide 63
www.sliderbase.com

## Slide 64
www.sliderbase.com

## Slide 65
Direct Reading Survey Meters and Counters: Useful in identifying source of exposures recorded by personal dosimeters, and in evaluating potential sources, such as surface or sample contamination, source leakage, inadequate decontamination procedures, background radiation.
Common types:
Alpha  Proportional or Scintillation counters Beta, gamma  Geiger-Mueller or Proportional counters X-ray, Gamma  Ionization chambers Neutrons  Proportional counters
www.sliderbase.com

## Slide 66
www.sliderbase.com

## Slide 67
Continuous Monitors: Continuous direct reading ionization detectors (same detectors as above) can provide read-out and/or alarm to monitor hazardous locations and alert workers to leakage, thereby preventing exposures.
Long-Term Samplers: Used to measure average exposures over a longer time period. For example, charcoal canisters or electrets are set out for days to months to measure radon in basements (should be <4 pCi/L).
www.sliderbase.com

## Slide 68: Elements of Radiation Protection Program
Monitoring of exposures: Personal, area, and screening measurements; Medical/biologic monitoring.
Task-Specific Procedures and Controls: Initial, periodic, and post-maintenance or other non-scheduled events. Engineering (shielding) vs. PPE vs. administrative controls. Including management and employee commitment and authority to enforce procedures and controls.
Emergency procedures: Response, "clean-up", post clean-up testing and spill control.
Training and Hazard Communications including signs, warning lights, lockout/tagout, etc. Criteria for need, design, and information given.
Material Handling: Receiving, inventory control, storage, and disposal.
www.sliderbase.com