## Slide 1: Static and Kinetic Friction
Nerik Yakubov Robert Magee David Chen
www.sliderbase.com

## Slide 2: Instructional Objectives
Distinguish the Difference Between Static & Kinetic Friction
Solve Problems Involving Friction Effects
www.sliderbase.com

## Slide 3: What is Friction?
Force that acts oppose the relative motion of two surfaces
High for dry and rough surfaces
Low for smooth and wet surfaces
www.sliderbase.com

## Slide 4: Free Body Diagram
Normal Force FN
Friction Force ff
Applied Force F
Gravity Force Fg
Fg = mg
FN = Fg
ff = F
www.sliderbase.com

## Slide 5: Static Friction
FN
fs
F
Fg
The Force of Static Friction keeps a stationary object at rest!
www.sliderbase.com

## Slide 6: Kinetic Friction
FN
fk
F
Fg
Once the Force of Static Friction is overcome, the Force of Kinetic Friction is what slows down a moving object!
Motion
www.sliderbase.com

## Slide 7: Types of Friction
I better be safe Ump!!
To initiate motion of the box the man must overcome the Force of Static Friction
Upon sliding, the baseball player will come to a complete stop due to the Force of Kinetic Friction
www.sliderbase.com

## Slide 8: Static & Kinetic Friction Coefficients
Material | Coefficient of Static Friction S | Coefficient of Kinetic Friction S
Rubber on Glass | 2.0+ | 2.0
Rubber on Concrete | 1.0 | 0.8
Steel on Steel | 0.74 | 0.57
Wood on Wood | 0.25 – 0.5 | 0.2
Metal on Metal | 0.15 | 0.06
Ice on Ice | 0.1 | 0.03
Synovial Joints in Humans | 0.01 | 0.003
www.sliderbase.com

## Slide 9: Static VS. Kinetic Friction
www.sliderbase.com

## Slide 10: Static Friction Lab Procedure
Connect the force detector to a block of wood
Pull gently on the force sensor unit the block begins to move
Move the block slowly with constant force
www.sliderbase.com

## Slide 11: Ideal Result
www.sliderbase.com

## Slide 12: Kinetic Friction Lab Procedure
Line up the block with the motion detector
Push the block gently toward the motion detector so that it comes to a stop approximately 1 foot away from it
From the velocity curve determine the deceleration of the block
Calculate the Force of Kinetic Friction
Determine the coefficient of Kinetic Friction
Wooden block
Push
www.sliderbase.com

## Slide 13: Application Analysis
An empty cart is being rolled across a warehouse floor. If the cart was filled, the force of kinetic friction between the cart and the floor would
  Decrease
  Increase
  Remain the same
www.sliderbase.com

## Slide 14: Application Analysis
Sand is often placed on an icy road because the sand:
  Decreases the coefficient of friction between the tires of a car and the road
  Increases the coefficient of friction between the tires of a car and the road
  Decrease the gravitational force on a car
  Increases the normal force of a car on the road
www.sliderbase.com