## Slide 1: Measuring
Volume
Temperature
Mass
Notes: Measuring
Volume
Temperature
Mass

## Slide 2: Reading the Meniscus
Always read volume from the bottom of the meniscus. The meniscus is the curved surface of a liquid in a narrow cylindrical container.
Notes: Reading the Meniscus
Always read volume from the bottom of the meniscus. The meniscus is the curved surface of a liquid in a narrow cylindrical container.

## Slide 3: Try to avoid parallax errors.
Parallax errors arise when a meniscus or needle is viewed from an angle rather than from straight-on at eye level.
Correct: Viewing the meniscus at eye level
Incorrect: viewing the meniscus from an angle
Notes: Try to avoid parallax errors.
Parallax errors arise when a meniscus or needle is viewed from an angle rather than from straight-on at eye level.
Correct: Viewing the meniscus at eye level
Incorrect: viewing the meniscus from an angle

## Slide 4: Graduated Cylinders
The glass cylinder has etched marks to indicate volumes, a pouring lip, and quite often, a plastic bumper to prevent breakage.
Notes: Graduated Cylinders
The glass cylinder has etched marks to indicate volumes, a pouring lip, and quite often, a plastic bumper to prevent breakage.

## Slide 5: Measuring Volume
Determine the volume contained in a graduated cylinder by reading the bottom of the meniscus at eye level.
Read the volume using all certain digits and one uncertain digit.
  Certain digits are determined from the calibration marks on the cylinder.
  The uncertain digit (the last digit of the reading) is estimated.
Notes: Measuring Volume
Determine the volume contained in a graduated cylinder by reading the bottom of the meniscus at eye level.
Read the volume using all certain digits and one uncertain digit.
Certain digits are determined from the calibration marks on the cylinder.
The uncertain digit (the last digit of the reading) is estimated.

## Slide 6: Use the graduations to find all certain digits
There are two unlabeled graduations below the meniscus, and each graduation represents 1 mL, so the certain digits of the reading are…
52 mL.
Notes: Use the graduations to find all certain digits
There are two unlabeled graduations below the meniscus, and each graduation represents 1 mL, so the certain digits of the reading are…
52 mL.

## Slide 7: Estimate the uncertain digit and take a reading
The meniscus is about eight tenths of the way to the next graduation, so the final digit in the reading is .
The volume in the graduated cylinder is
0.8 mL
52.8 mL.
Notes: Estimate the uncertain digit and take a reading
The meniscus is about eight tenths of the way to the next graduation, so the final digit in the reading is .
The volume in the graduated cylinder is
0.8 mL
52.8 mL.

## Slide 8: 10 mL Graduate
What is the volume of liquid in the graduate?
_ . _ _ mL
6
2
6
Notes: 10 mL Graduate
What is the volume of liquid in the graduate?
_ . _ _ mL
6
2
6

## Slide 9: 25mL graduated cylinder
What is the volume of liquid in the graduate?
_ _ . _ mL
1
1
5
Notes: 25mL graduated cylinder
What is the volume of liquid in the graduate?
_ _ . _ mL
1
1
5

## Slide 10: 100mL graduated cylinder
What is the volume of liquid in the graduate?
_ _ . _ mL
5
2
7
Notes: 100mL graduated cylinder
What is the volume of liquid in the graduate?
_ _ . _ mL
5
2
7

## Slide 11: Self Test
Examine the meniscus below and determine the volume of liquid contained in the graduated cylinder.
The cylinder contains:
_ _ . _ mL
7
6
0
Notes: Self Test
Examine the meniscus below and determine the volume of liquid contained in the graduated cylinder.
The cylinder contains:
_ _ . _ mL
7
6
0

## Slide 12: The Thermometer
Determine the temperature by reading the scale on the thermometer at eye level.
Read the temperature by using all certain digits and one uncertain digit.
Certain digits are determined from the calibration marks on the thermometer.
The uncertain digit (the last digit of the reading) is estimated.
On most thermometers encountered in a general chemistry lab, the tenths place is the uncertain digit.
Notes: The Thermometer
Determine the temperature by reading the scale on the thermometer at eye level.
Read the temperature by using all certain digits and one uncertain digit.
Certain digits are determined from the calibration marks on the thermometer.
The uncertain digit (the last digit of the reading) is estimated.
On most thermometers encountered in a general chemistry lab, the tenths place is the uncertain digit.

## Slide 13: Do not allow the tip to touch the walls or the bottom of the flask.
If the thermometer bulb touches the flask, the temperature of the glass will be measured instead of the temperature of the solution. Readings may be incorrect, particularly if the flask is on a hotplate or in an ice bath.
Notes: Do not allow the tip to touch the walls or the bottom of the flask.
If the thermometer bulb touches the flask, the temperature of the glass will be measured instead of the temperature of the solution. Readings may be incorrect, particularly if the flask is on a hotplate or in an ice bath.

## Slide 14: Reading the Thermometer
Determine the readings as shown below on Celsius thermometers:
_ _ . _ C
_ _ . _ C
8
7
4
3
5
0
Notes: Reading the Thermometer
Determine the readings as shown below on Celsius thermometers:
_ _ . _ C
_ _ . _ C
8
7
4
3
5
0

## Slide 15: Measuring Mass - The Beam Balance
Our balances have 4 beams – the uncertain digit is the thousandths place ( _ _ _ . _ _ X)
Notes: Measuring Mass - The Beam Balance
Our balances have 4 beams – the uncertain digit is the thousandths place ( _ _ _ . _ _ X)

## Slide 16: Balance Rules
In order to protect the balances and ensure accurate results, a number of rules should be followed:
Always check that the balance is level and zeroed before using it.
Never weigh directly on the balance pan. Always use a piece of weighing paper to protect it.
Do not weigh hot or cold objects.
Clean up any spills around the balance immediately.
Notes: Balance Rules
In order to protect the balances and ensure accurate results, a number of rules should be followed:
Always check that the balance is level and zeroed before using it.
Never weigh directly on the balance pan. Always use a piece of weighing paper to protect it.
Do not weigh hot or cold objects.
Clean up any spills around the balance immediately.

## Slide 17: Mass and Significant Figures
Determine the mass by reading the riders on the beams at eye level.
Read the mass by using all certain digits and one uncertain digit.
The uncertain digit (the last digit of the reading) is estimated.
On our balances, the thousandths place is uncertain.
Notes: Mass and Significant Figures
Determine the mass by reading the riders on the beams at eye level.
Read the mass by using all certain digits and one uncertain digit.
The uncertain digit (the last digit of the reading) is estimated.
On our balances, the thousandths place is uncertain.

## Slide 18: Determining Mass
1. Place object on pan
2. Move riders along beam, starting with the largest, until the pointer is at the zero mark
Notes: Determining Mass
1. Place object on pan
2. Move riders along beam, starting with the largest, until the pointer is at the zero mark

## Slide 19: Check to see that the balance scale is at zero
Notes: Check to see that the balance scale is at zero

## Slide 20: Read Mass
_ _ _ . _ _ _
1
1
4
? ? ?
Notes: Read Mass
_ _ _ . _ _ _
1
1
4
? ? ?

## Slide 21: Read Mass More Closely
_ _ _ . _ _ _
1
1
4
4
9
7
Notes: Read Mass More Closely
_ _ _ . _ _ _
1
1
4
4
9
7