## Slide 1: WELL LOG (The Bore Hole Image)
What is well Logging
Well log is a continuous record of measurement made in bore hole respond to variation in some physical properties of rocks through which the bore hole is drilled.
Traditionally Logs are display on girded papers shown in figure.
Now a days the log may be taken as films, images, and in digital format.
Notes: WELL LOG (The Bore Hole Image)
What is well Logging
Well log is a continuous record of measurement made in bore hole respond to variation in some physical properties of rocks through which the bore hole is drilled.
Traditionally Logs are display on girded papers shown in figure.
Now a days the log may be taken as films, images, and in digital format.
WELL LOG (The Bore Hole Image)
What is well Logging
Well log is a continuous record of measurement made in bore hole respond to variation in some physical properties of rocks through which the bore hole is drilled.
Traditionally Logs are display on girded papers shown in figure.
Now a days the log may be taken as films, images, and in digital format.

## Slide 2: HISTORY
1912 Conrad Schlumberger give the idea of using electrical measurements to map subsurface rock bodies.
in 1919 Conrad Schlumberger and his brother Marcel begin work on well logs.
The first electrical resistivity well log was taken in France, in 1927.
The instrument which was use for this purpose is called SONDE, the sond was stopped at periodic intervals in bore hole and the and resistivity was plotted on graph paper.
In 1929 the electrical resistivity logs are introduce on commercial scale in Venezuela, USA and Russia
For correlation and identification of Hydrocarbon bearing strata.
The photographic – film recorder was developed in 1936 the curves were SN,LN AND LAT
The dip meter log were developed in 1930
The Gamma Ray and Neutron Log were begin in 1941
Notes: HISTORY
1912 Conrad Schlumberger give the idea of using electrical measurements to map subsurface rock bodies.
in 1919 Conrad Schlumberger and his brother Marcel begin work on well logs.
The first electrical resistivity well log was taken in France, in 1927.
The instrument which was use for this purpose is called SONDE, the sond was stopped at periodic intervals in bore hole and the and resistivity was plotted on graph paper.
In 1929 the electrical resistivity logs are introduce on commercial scale in Venezuela, USA and Russia
For correlation and identification of Hydrocarbon bearing strata.
The photographic – film recorder was developed in 1936 the curves were SN,LN AND LAT
The dip meter log were developed in 1930
The Gamma Ray and Neutron Log were begin in 1941
HISTORY
1912 Conrad Schlumberger give the idea of using electrical measurements to map subsurface rock bodies.
in 1919 Conrad Schlumberger and his brother Marcel begin work on well logs.
The first electrical resistivity well log was taken in France, in 1927.
The instrument which was use for this purpose is called SONDE, the sond was stopped at periodic intervals in bore hole and the and resistivity was plotted on graph paper.
In 1929 the electrical resistivity logs are introduce on commercial scale in Venezuela, USA and Russia
For correlation and identification of Hydrocarbon bearing strata.
The photographic – film recorder was developed in 1936 the curves were SN,LN AND LAT
The dip meter log were developed in 1930
The Gamma Ray and Neutron Log were begin in 1941

## Slide 3: LOGGING UNITS
Logging service companies utilize a variety of logging units, depending on the location (onshore or offshore) and requirements of the logging run. Each unit will contain the following components:
logging cable
winch to raise and lower the cable in the well
self-contained 120-volt AC generator
set of surface control panels
set of downhole tools (sondes and cartridges)
digital recording system
Notes: LOGGING UNITS
Logging service companies utilize a variety of logging units, depending on the location (onshore or offshore) and requirements of the logging run. Each unit will contain the following components:
logging cable
winch to raise and lower the cable in the well
self-contained 120-volt AC generator
set of surface control panels
set of downhole tools (sondes and cartridges)
digital recording system
LOGGING UNITS
Logging service companies utilize a variety of logging units, depending on the location (onshore or offshore) and requirements of the logging run. Each unit will contain the following components:
logging cable
winch to raise and lower the cable in the well
self-contained 120-volt AC generator
set of surface control panels
set of downhole tools (sondes and cartridges)
digital recording system

## Slide 4: Work Flow Chart
Notes: Work Flow Chart
Work Flow Chart

## Slide 6
depth to lithological boundaries
lithology identification
minerals grade/quality
inter-borehole correlation
structure mapping
dip determination
rock strength
in-situ stress orientation
fracture frequency
porosity
fluid salinity
Notes: depth to lithological boundaries
lithology identification
minerals grade/quality
inter-borehole correlation
structure mapping
dip determination
rock strength
in-situ stress orientation
fracture frequency
porosity
fluid salinity
depth to lithological boundaries
lithology identification
minerals grade/quality
inter-borehole correlation
structure mapping
dip determination
rock strength
in-situ stress orientation
fracture frequency
porosity
fluid salinity

## Slide 7: Depth Of Investigation Of Logging Tools
Notes: Depth Of Investigation Of Logging Tools
Depth Of Investigation Of Logging Tools

## Slide 8: LOG INTERPRETATION OBJECTIVES
The objective of log interpretation depends very much on the user. Quantitative analysis of well logs provides the analyst with values for a variety of primary parameters, such as:
porosity
water saturation, fluid type (oil/gas/water)
lithology
permeability
From these, many corollary parameters can be derived by integration (and other means) to arrive at values for:
hydrocarbons-in-place
reserves (the recoverable fraction of hydrocarbons in-place)
mapping reservoir parameters
But not all users of wireline logs have quantitative analysis as their objective. Many of them are more concerned with the geological and geophysical aspects. These users are interested in interpretation for:
well-to-well correlation
facies analysis
regional structural and sedimentary history
In quantitative log analysis, the objective is to define
the type of reservoir (lithology)
its storage capacity (porosity)
its hydrocarbon type and content (saturation)
its producibility (permeability)
Notes: LOG INTERPRETATION OBJECTIVES
The objective of log interpretation depends very much on the user. Quantitative analysis of well logs provides the analyst with values for a variety of primary parameters, such as:
porosity
water saturation, fluid type (oil/gas/water)
lithology
permeability
From these, many corollary parameters can be derived by integration (and other means) to arrive at values for:
hydrocarbons-in-place
reserves (the recoverable fraction of hydrocarbons in-place)
mapping reservoir parameters
But not all users of wireline logs have quantitative analysis as their objective. Many of them are more concerned with the geological and geophysical aspects. These users are interested in interpretation for:
well-to-well correlation
facies analysis
regional structural and sedimentary history
In quantitative log analysis, the objective is to define
the type of reservoir (lithology)
its storage capacity (porosity)
its hydrocarbon type and content (saturation)
its producibility (permeability)
LOG INTERPRETATION OBJECTIVES
The objective of log interpretation depends very much on the user. Quantitative analysis of well logs provides the analyst with values for a variety of primary parameters, such as:
porosity
water saturation, fluid type (oil/gas/water)
lithology
permeability
From these, many corollary parameters can be derived by integration (and other means) to arrive at values for:
hydrocarbons-in-place
reserves (the recoverable fraction of hydrocarbons in-place)
mapping reservoir parameters
But not all users of wireline logs have quantitative analysis as their objective. Many of them are more concerned with the geological and geophysical aspects. These users are interested in interpretation for:
well-to-well correlation
facies analysis
regional structural and sedimentary history
In quantitative log analysis, the objective is to define
the type of reservoir (lithology)
its storage capacity (porosity)
its hydrocarbon type and content (saturation)
its producibility (permeability)

## Slide 9: GAMMA RAY LOG
Gamma Rays are high-energy electromagnetic waves which are emitted by atomic nuclei as a form of radiation
Gamma ray log is measurement of natural radioactivity in formation verses depth.
It measures the radiation emitting from naturally occurring U, Th, and K.
It is also known as shale log.
GR log reflects shale or clay content.
Clean formations have low radioactivity level.
Correlation between wells,
Determination of bed boundaries,
Evaluation of shale content within a formation,
Mineral analysis,
Depth control for log tie-ins, side-wall coring, or perforating.
Particularly useful for defining shale beds when the sp is featureless
GR log can be run in both open and cased hole
Notes: GAMMA RAY LOG
Gamma Rays are high-energy electromagnetic waves which are emitted by atomic nuclei as a form of radiation
Gamma ray log is measurement of natural radioactivity in formation verses depth.
It measures the radiation emitting from naturally occurring U, Th, and K.
It is also known as shale log.
GR log reflects shale or clay content.
Clean formations have low radioactivity level.
Correlation between wells,
Determination of bed boundaries,
Evaluation of shale content within a formation,
Mineral analysis,
Depth control for log tie-ins, side-wall coring, or perforating.
Particularly useful for defining shale beds when the sp is featureless
GR log can be run in both open and cased hole
GAMMA RAY LOG
Gamma Rays are high-energy electromagnetic waves which are emitted by atomic nuclei as a form of radiation
Gamma ray log is measurement of natural radioactivity in formation verses depth.
It measures the radiation emitting from naturally occurring U, Th, and K.
It is also known as shale log.
GR log reflects shale or clay content.
Clean formations have low radioactivity level.
Correlation between wells,
Determination of bed boundaries,
Evaluation of shale content within a formation,
Mineral analysis,
Depth control for log tie-ins, side-wall coring, or perforating.
Particularly useful for defining shale beds when the sp is featureless
GR log can be run in both open and cased hole

## Slide 10: Spontaneous Potential Log (SP)
The spontaneous potential (SP) curve records the naturally occurring electrical potential (voltage) produced by the interaction of formation connate water, conductive drilling fluid, and shale
The SP curve reflects a difference in the electrical potential between a movable electrode in the borehole and a fixed reference electrode at the surface
Though the SP is used primarily as a lithology indicator and as a correlation tool, it has other uses as well:
  permeability indicator,
  shale volume indicator
  porosity indicator, and
  measurement of Rw (hence formation water salinity).
Notes: Spontaneous Potential Log (SP)
The spontaneous potential (SP) curve records the naturally occurring electrical potential (voltage) produced by the interaction of formation connate water, conductive drilling fluid, and shale
The SP curve reflects a difference in the electrical potential between a movable electrode in the borehole and a fixed reference electrode at the surface
Though the SP is used primarily as a lithology indicator and as a correlation tool, it has other uses as well:
permeability indicator,
shale volume indicator
porosity indicator, and
measurement of Rw (hence formation water salinity).
Spontaneous Potential Log (SP)
The spontaneous potential (SP) curve records the naturally occurring electrical potential (voltage) produced by the interaction of formation connate water, conductive drilling fluid, and shale
The SP curve reflects a difference in the electrical potential between a movable electrode in the borehole and a fixed reference electrode at the surface
Though the SP is used primarily as a lithology indicator and as a correlation tool, it has other uses as well:
permeability indicator,
shale volume indicator
porosity indicator, and
measurement of Rw (hence formation water salinity).

## Slide 11: Neutron Logging
The Neutron Log is primarily used to evaluate formation porosity, but the fact that it is really just a hydrogen detector should always be kept in mind
It is used to detect gas in certain situations, exploiting the lower hydrogen density, or hydrogen index
The Neutron Log can be summarized as the continuous measurement of the induced radiation produced by the bombardment of that formation with a neutron source contained in the logging tool which sources emit fast neutrons that are eventually slowed by collisions with hydrogen atoms until they are captured (think of a billiard ball metaphor where the similar size of the particles is a factor). The capture results in the emission of a secondary gamma ray; some tools, especially older ones, detect the capture gamma ray (neutron-gamma log). Other tools detect intermediate (epithermal) neutrons or slow (thermal) neutrons (both referred to as neutron-neutron logs). Modern neutron tools most commonly count thermal neutrons with an He-3 type detector.
Notes: Neutron Logging
The Neutron Log is primarily used to evaluate formation porosity, but the fact that it is really just a hydrogen detector should always be kept in mind
It is used to detect gas in certain situations, exploiting the lower hydrogen density, or hydrogen index
The Neutron Log can be summarized as the continuous measurement of the induced radiation produced by the bombardment of that formation with a neutron source contained in the logging tool which sources emit fast neutrons that are eventually slowed by collisions with hydrogen atoms until they are captured (think of a billiard ball metaphor where the similar size of the particles is a factor). The capture results in the emission of a secondary gamma ray; some tools, especially older ones, detect the capture gamma ray (neutron-gamma log). Other tools detect intermediate (epithermal) neutrons or slow (thermal) neutrons (both referred to as neutron-neutron logs). Modern neutron tools most commonly count thermal neutrons with an He-3 type detector.
Neutron Logging
The Neutron Log is primarily used to evaluate formation porosity, but the fact that it is really just a hydrogen detector should always be kept in mind
It is used to detect gas in certain situations, exploiting the lower hydrogen density, or hydrogen index
The Neutron Log can be summarized as the continuous measurement of the induced radiation produced by the bombardment of that formation with a neutron source contained in the logging tool which sources emit fast neutrons that are eventually slowed by collisions with hydrogen atoms until they are captured (think of a billiard ball metaphor where the similar size of the particles is a factor). The capture results in the emission of a secondary gamma ray; some tools, especially older ones, detect the capture gamma ray (neutron-gamma log). Other tools detect intermediate (epithermal) neutrons or slow (thermal) neutrons (both referred to as neutron-neutron logs). Modern neutron tools most commonly count thermal neutrons with an He-3 type detector.

## Slide 12: The Density Log
The formation density log is a porosity log that measures electron density of a formation
Dense formations absorb many gamma rays, while low-density formations absorb fewer. Thus, high-count rates at the detectors indicate low-density formations, whereas low count rates at the detectors indicate high-density formations.
Therefore, scattered gamma rays reaching the detector is an indication of formation Density.
Scale and units:
The most frequently used scales are a range of 2.0 to 3.0 gm/cc or 1.95 to 2.95 gm/cc across two tracks.
A density derived porosity curve is sometimes present in tracks #2 and #3 along with the bulk density (rb) and correction (Dr) curves. Track #1 contains a gamma ray log and caliper.
Notes: The Density Log
The formation density log is a porosity log that measures electron density of a formation
Dense formations absorb many gamma rays, while low-density formations absorb fewer. Thus, high-count rates at the detectors indicate low-density formations, whereas low count rates at the detectors indicate high-density formations.
Therefore, scattered gamma rays reaching the detector is an indication of formation Density.
Scale and units:
The most frequently used scales are a range of 2.0 to 3.0 gm/cc or 1.95 to 2.95 gm/cc across two tracks.
A density derived porosity curve is sometimes present in tracks #2 and #3 along with the bulk density (rb) and correction (Dr) curves. Track #1 contains a gamma ray log and caliper.
The Density Log
The formation density log is a porosity log that measures electron density of a formation
Dense formations absorb many gamma rays, while low-density formations absorb fewer. Thus, high-count rates at the detectors indicate low-density formations, whereas low count rates at the detectors indicate high-density formations.
Therefore, scattered gamma rays reaching the detector is an indication of formation Density.
Scale and units:
The most frequently used scales are a range of 2.0 to 3.0 gm/cc or 1.95 to 2.95 gm/cc across two tracks.
A density derived porosity curve is sometimes present in tracks #2 and #3 along with the bulk density (rb) and correction (Dr) curves. Track #1 contains a gamma ray log and caliper.

## Slide 13: Resistivity Log
Basics about the Resistivity:
Resistivity measures the electric properties of the formation,
Resistivity is measured as, R in W per m,
Resistivity is the inverse of conductivity,
The ability to conduct electric current depends upon:
    The Volume of water,
    The Temperature of the formation,
    The Salinity of the formation
The Resistivity Log:
Resistivity logs measure the ability of rocks to
conduct electrical current and are scaled in units of ohm-
meters.
The Usage:
Resistivity logs are electric logs which are used to:
Determine Hydrocarbon versus Water-bearing zones,
Indicate Permeable zones,
Determine Resisitivity Porosity.
Notes: Resistivity Log
Basics about the Resistivity:
Resistivity measures the electric properties of the formation,
Resistivity is measured as, R in W per m,
Resistivity is the inverse of conductivity,
The ability to conduct electric current depends upon:
The Volume of water,
The Temperature of the formation,
The Salinity of the formation
The Resistivity Log:
Resistivity logs measure the ability of rocks to
conduct electrical current and are scaled in units of ohm-
meters.
The Usage:
Resistivity logs are electric logs which are used to:
Determine Hydrocarbon versus Water-bearing zones,
Indicate Permeable zones,
Determine Resisitivity Porosity.
Resistivity Log
Basics about the Resistivity:
Resistivity measures the electric properties of the formation,
Resistivity is measured as, R in W per m,
Resistivity is the inverse of conductivity,
The ability to conduct electric current depends upon:
The Volume of water,
The Temperature of the formation,
The Salinity of the formation
The Resistivity Log:
Resistivity logs measure the ability of rocks to
conduct electrical current and are scaled in units of ohm-
meters.
The Usage:
Resistivity logs are electric logs which are used to:
Determine Hydrocarbon versus Water-bearing zones,
Indicate Permeable zones,
Determine Resisitivity Porosity.

## Slide 14: Acoustic Log
Shahbaz Younis (Pakistan)
Acoustic tools measure the speed of sound waves in subsurface formations. While the acoustic log can be used to determine porosity in consolidated formations, it is also valuable in other applications, such as:
Indicating lithology (using the ratio of compressional velocity over shear velocity),
Determining integrated travel time (an important tool for seismic/wellbore correlation),
Correlation with other wells
Detecting fractures and evaluating secondary porosity,
Evaluating cement bonds between casing, and formation,
Detecting over-pressure,
Determining mechanical properties (in combination with the density log), and
Determining acoustic impedance (in combination with the density log).
Notes: Shahbaz Younis (Pakistan)
Acoustic tools measure the speed of sound waves in subsurface formations. While the acoustic log can be used to determine porosity in consolidated formations, it is also valuable in other applications, such as:
Indicating lithology (using the ratio of compressional velocity over shear velocity),
Determining integrated travel time (an important tool for seismic/wellbore correlation),
Correlation with other wells
Detecting fractures and evaluating secondary porosity,
Evaluating cement bonds between casing, and formation,
Detecting over-pressure,
Determining mechanical properties (in combination with the density log), and
Determining acoustic impedance (in combination with the density log).
Acoustic Log
Shahbaz Younis (Pakistan)
Acoustic tools measure the speed of sound waves in subsurface formations. While the acoustic log can be used to determine porosity in consolidated formations, it is also valuable in other applications, such as:
Indicating lithology (using the ratio of compressional velocity over shear velocity),
Determining integrated travel time (an important tool for seismic/wellbore correlation),
Correlation with other wells
Detecting fractures and evaluating secondary porosity,
Evaluating cement bonds between casing, and formation,
Detecting over-pressure,
Determining mechanical properties (in combination with the density log), and
Determining acoustic impedance (in combination with the density log).
Acoustic Log