## Slide 1: AS Biology Core Principles
The Electron Microscope
www.sliderbase.com
Notes: AS Biology Core Principles
The Electron Microscope
AS Biology Core Principles
The Electron Microscope

## Slide 2: Aims
Resolving power
The resolving power of light & electron microscopes
The difference between the light & electron microscope
Transmission & scanning electron microscopy
www.sliderbase.com
Notes: Aims
Resolving power
The resolving power of light & electron microscopes
The difference between the light & electron microscope
Transmission & scanning electron microscopy
Aims
Resolving power
The resolving power of light & electron microscopes
The difference between the light & electron microscope
Transmission & scanning electron microscopy

## Slide 3: Introduction
Microscopes magnify & resolve images
Microscopy began in 1665 when Robert Hooke coined the word ‘cells’ to describe the structure of cork
You need to know about 2 types of microscope - light & electron
You need to know how they work and the differences between them
‘Its not how much they magnify that is key - but how well they resolve…’
www.sliderbase.com
Notes: Introduction
Microscopes magnify & resolve images
Microscopy began in 1665 when Robert Hooke coined the word ‘cells’ to describe the structure of cork
You need to know about 2 types of microscope - light & electron
You need to know how they work and the differences between them
‘Its not how much they magnify that is key - but how well they resolve…’
Introduction
Microscopes magnify & resolve images
Microscopy began in 1665 when Robert Hooke coined the word ‘cells’ to describe the structure of cork
You need to know about 2 types of microscope - light & electron
You need to know how they work and the differences between them
‘Its not how much they magnify that is key - but how well they resolve…’

## Slide 4: Resolving Power
The limit of resolution of a microscope is the smallest distance between 2 points that can be seen using a microscope
This is a measure of the clarity of the image
A microscope with a high resolving power will allow 2 small objects which are close together to be seen as 2 distinct objects
www.sliderbase.com
Notes: Resolving Power
The limit of resolution of a microscope is the smallest distance between 2 points that can be seen using a microscope
This is a measure of the clarity of the image
A microscope with a high resolving power will allow 2 small objects which are close together to be seen as 2 distinct objects
Resolving Power
The limit of resolution of a microscope is the smallest distance between 2 points that can be seen using a microscope
This is a measure of the clarity of the image
A microscope with a high resolving power will allow 2 small objects which are close together to be seen as 2 distinct objects

## Slide 5: Resolving Power
Resolving power is inversely proportional to the wavelength of the radiation it uses
www.sliderbase.com
Notes: Resolving Power
Resolving power is inversely proportional to the wavelength of the radiation it uses
Resolving Power
Resolving power is inversely proportional to the wavelength of the radiation it uses

## Slide 6: The Light Microscope
Series of lenses through which ordinary white light can be focused
Optical microscopes can not resolve 2 points closer together than about half (0.45) the wavelength of the light used (450-600nm)
How close is this?
www.sliderbase.com
Notes: The Light Microscope
Series of lenses through which ordinary white light can be focused
Optical microscopes can not resolve 2 points closer together than about half (0.45) the wavelength of the light used (450-600nm)
How close is this?
The Light Microscope
Series of lenses through which ordinary white light can be focused
Optical microscopes can not resolve 2 points closer together than about half (0.45) the wavelength of the light used (450-600nm)
How close is this?

## Slide 7: The Light Microscope
The total magnification is the eyepiece magnification multiplied by the objective magnification
The maximum magnification of a light microscope is x1500
What can it be used for?
What can it not be used for?
www.sliderbase.com
Notes: The Light Microscope
The total magnification is the eyepiece magnification multiplied by the objective magnification
The maximum magnification of a light microscope is x1500
What can it be used for?
What can it not be used for?
The Light Microscope
The total magnification is the eyepiece magnification multiplied by the objective magnification
The maximum magnification of a light microscope is x1500
What can it be used for?
What can it not be used for?

## Slide 8: The Electron Microscope
Electrons (negatively charged, very small particles) can behave as waves
The wavelength of electrons is about 0.005nm
What will this mean for the limit of resolution?
Electrons are ‘fired’ from an electron gun at the specimen and onto a fluorescent screen or photographic plate
Where is this technique commonly used?
There are 2 types of electron microscopy - transmission and scanning
Both focus an electron beam onto the specimen using electromagnets
www.sliderbase.com
Notes: The Electron Microscope
Electrons (negatively charged, very small particles) can behave as waves
The wavelength of electrons is about 0.005nm
What will this mean for the limit of resolution?
Electrons are ‘fired’ from an electron gun at the specimen and onto a fluorescent screen or photographic plate
Where is this technique commonly used?
There are 2 types of electron microscopy - transmission and scanning
Both focus an electron beam onto the specimen using electromagnets
The Electron Microscope
Electrons (negatively charged, very small particles) can behave as waves
The wavelength of electrons is about 0.005nm
What will this mean for the limit of resolution?
Electrons are ‘fired’ from an electron gun at the specimen and onto a fluorescent screen or photographic plate
Where is this technique commonly used?
There are 2 types of electron microscopy - transmission and scanning
Both focus an electron beam onto the specimen using electromagnets

## Slide 9: Transmission Electron Microscope (TEM)
In transmission EM the electrons pass through the specimen
Specimen needs to be extremely thin - 10nm to 100nm
TEM can magnify objects up to 500 000 times
TEM has made it possible to see the details of and discover new organelles - see page 9 in Collins
www.sliderbase.com
Notes: Transmission Electron Microscope (TEM)
In transmission EM the electrons pass through the specimen
Specimen needs to be extremely thin - 10nm to 100nm
TEM can magnify objects up to 500 000 times
TEM has made it possible to see the details of and discover new organelles - see page 9 in Collins
Transmission Electron Microscope (TEM)
In transmission EM the electrons pass through the specimen
Specimen needs to be extremely thin - 10nm to 100nm
TEM can magnify objects up to 500 000 times
TEM has made it possible to see the details of and discover new organelles - see page 9 in Collins

## Slide 10: Transmission Electron Microscope (TEM)
Cells or tissues are killed and chemically ‘fixed’ in a complicated and harsh treatment (in full detail in table 3.1 pg 52 Rowland)
How does this differ to light microscopy?
This treatment can result in alterations to the cell - known as artefacts
What will this mean for the images produced?
www.sliderbase.com
Notes: Transmission Electron Microscope (TEM)
Cells or tissues are killed and chemically ‘fixed’ in a complicated and harsh treatment (in full detail in table 3.1 pg 52 Rowland)
How does this differ to light microscopy?
This treatment can result in alterations to the cell - known as artefacts
What will this mean for the images produced?
Transmission Electron Microscope (TEM)
Cells or tissues are killed and chemically ‘fixed’ in a complicated and harsh treatment (in full detail in table 3.1 pg 52 Rowland)
How does this differ to light microscopy?
This treatment can result in alterations to the cell - known as artefacts
What will this mean for the images produced?

## Slide 11: Transmission Electron Microscope (TEM)
Transmission electron micrograph of epithelial cells from a rat small intestine.
Scale bar = 5 mm.
www.sliderbase.com
Notes: Transmission Electron Microscope (TEM)
Transmission electron micrograph of epithelial cells from a rat small intestine.
Scale bar = 5 mm.
Transmission Electron Microscope (TEM)
Transmission electron micrograph of epithelial cells from a rat small intestine.
Scale bar = 5 mm.

## Slide 12: Scanning Electron Microscope (SEM)
In Scanning EM microscopes the electrons bounce off the surface of the specimen
Produce images with a three-dimensional appearance
Allow detailed study of surfaces
www.sliderbase.com
Notes: Scanning Electron Microscope (SEM)
In Scanning EM microscopes the electrons bounce off the surface of the specimen
Produce images with a three-dimensional appearance
Allow detailed study of surfaces
Scanning Electron Microscope (SEM)
In Scanning EM microscopes the electrons bounce off the surface of the specimen
Produce images with a three-dimensional appearance
Allow detailed study of surfaces

## Slide 13: Scanning Electron Microscope (SEM)
Now watch the following clip explaining SEM
www.sliderbase.com
Notes: Scanning Electron Microscope (SEM)
Now watch the following clip explaining SEM
Scanning Electron Microscope (SEM)
Now watch the following clip explaining SEM

## Slide 14: Scanning Electron Microscope (SEM)
www.sliderbase.com
Notes: Scanning Electron Microscope (SEM)
Scanning Electron Microscope (SEM)

## Slide 15: Links
www.learn.co.uk/
www.microscopy-uk.org.uk/intro/index.html
www.mwrn.com/feature/education.asp
http://www.feic.com/support/tem/transmis.htm
http://anka.livstek.lth.se:2080/microscopy/foodmicr.htm
www.sliderbase.com
Notes: Links
www.learn.co.uk/
www.microscopy-uk.org.uk/intro/index.html
www.mwrn.com/feature/education.asp
http://www.feic.com/support/tem/transmis.htm
http://anka.livstek.lth.se:2080/microscopy/foodmicr.htm
Links
www.learn.co.uk/
www.microscopy-uk.org.uk/intro/index.html
www.mwrn.com/feature/education.asp
http://www.feic.com/support/tem/transmis.htm
http://anka.livstek.lth.se:2080/microscopy/foodmicr.htm

## Slide 16: Light & Electron Microscopes
Feature | Light Microscope | Electron Microscope
Radiation used |  | 
Radiation source |  | 
Nature of lenses |  | 
Lenses used |  | 
Image seen |  | 
Radiation medium |  | 
Magnification |  | 
Limit of resolution |  | 
What it can show |  | 
Copy & complete the following table
www.sliderbase.com
Notes: Light & Electron Microscopes
Copy & complete the following table
Light & Electron Microscopes
Copy & complete the following table